1. The Model:

The model is defined by the state variables, the error and actuators.
a) State Variables :
- position(x and y coordinates)
- orientation(psi)
- velocity(v)

b) Errors:
- Cross Track Error (cte)
- Orientation Error (epsi)

c) Actuators:
- steering wheel(delta)
- acceleration(a)

State update:
The state of the car is updated over time as per the following equations:

   x_[t+1] = x[t] + v[t] * cos(psi[t]) * dt
   y_[t+1] = y[t] + v[t] * sin(psi[t]) * dt
   psi_[t+1] = psi[t] + v[t] / Lf * delta[t] * dt
   v_[t+1] = v[t] + a[t] * dt

   Lf - this is the length from front of vehicle to its Center-of-Gravity

We can also predict the next cte and epsi based on our actuations.

cte_[t+1] = cte[t] - v[t] * sin(epsi[t] ) * dt
epsi_[t+1] = epsi[t] + v[t] / Lf * (-delta[t] ) * dt

2. TimeStep Length & Elapsed Duration (N & dt):

The prediction horizon is the duration over which future predictions are made. This is denoted by T. T is the product of two other variables, N and dt where N is the number of time steps in the horizon and dt is how much time elapses between actuations.

For tuning these hyper parameters, a lot of experiments were done. Initially we started with large values of T like 2 while dt was set to 0.05. After experimenting a while, the following values were found to be reliable: N=15, dt=0.1, T=1.5 .

3. Polynomial Fitting and MPC Preprocessing

As a 3-order polynomial can fit most trajectories, we fitted a 3-order polynomial to the way points returned by the simulator using the polyfit function.

4. Model Predictive Control with Latency

Latency is handled by predicting the state of the vehicle the length of time of the latency in the future and using that in as the input state. This means we calculate the new car's new_px and new_py and new_psi at latency time and then map the waypoints from global coordinates to new_vehicle coordinates.
Then its fed into the solver. The val will have the predicted optimum actuation values which are at 100ms in the future.